## Slide 1
Dual-ISP Network Assessment
and Subnet Remediation
Multi-vantage-point discovery, overlapping RFC 1918 remediation, and dual-homed NAS reconfiguration across two independent residential ISP links
Vijaysingh Puwar
M.S. Cybersecurity · Seidenberg School of CSIS · Pace University
THE DEFECT
Gateway A 192.168.0.1/24
Gateway B 192.168.0.1/24
two physical networks
one address plan
Notes: Two independently provisioned ISP services, each on its own gateway, both left on the vendor default 192.168.0.0/24 with gateway 192.168.0.1. A NAS sat in both networks at once. Nothing was down, which is exactly why it survived so long.

## Slide 2
The environment
Consumer hardware, two routed domains, one appliance in both of them.
2
independent ISP services
each terminated on its own gateway
2
consumer gateways
identical vendor-default address plan
1
NAS, dual-homed
one interface in each domain
3
discovery vantage points
spanning both domains
Hardware
TP-Link Archer AX53 (Gateway A) · TP-Link Archer AX10 (Gateway B, PPPoE WAN) · Synology DS423+ (dual NIC, 1 Gb/s each)
Two unmanaged switches · Windows 11 workstation · two Mac minis · an unenumerated population of wireless clients
Notes: Everything here is consumer-grade. The value of the project is not the hardware; it is that the address-plan defect is a real one that appears in enterprise environments after mergers and over VPN.

## Slide 3
One address plan, two networks
Both gateways shipped with the same default and were never changed.
OBSERVED STATE
Gateway A 192.168.0.1/24
Gateway B 192.168.0.1/24
NAS LAN 1 192.168.0.2
NAS LAN 2 192.168.0.242
DHCP active on both, overlapping scopes
Physically separate at Layer 2. Logically indistinguishable at Layer 3.
What that actually costs you
Ambiguous management plane — both gateways answer at 192.168.0.1, so a config change can land on the wrong device with no warning.
Address collision under DHCP — two servers lease from overlapping ranges and neither can detect the other's conflicts.
Non-deterministic routing on the multi-homed NAS — two interfaces with no prefix-based basis for selection.
Degraded diagnosability — inventories disagree, and the obvious explanations all point away from the real fault.
Notes: Note the ordering: the management-plane risk is the one that can actually destroy something, because you can reconfigure the wrong router without ever knowing.

## Slide 4
Why it never looked like a defect
Each domain was internally consistent, so nothing ever broke.
1
No outage
Every device reached the internet and its own local peers. There was no failure to report, so there was no trigger to investigate.
2
Symptoms invited the wrong diagnosis
Hosts that could not reach each other while apparently sharing a subnet reads as client isolation or a firewall policy — both of which lead troubleshooting away from the address plan.
3
Discovery contradicted itself
Scans from different machines returned different device lists for the same declared network, which looks like tooling error rather than evidence.
Latent address-plan defects are not found during quiet periods. They are found under time pressure, during an unrelated change.
Notes: This is the argument for periodic assessment of environments believed to be working correctly.

## Slide 5
Discovery pipeline
One logical pipeline, implemented twice, so heterogeneous results stay comparable.
1
Interface
enumeration
Local adapters, prefixes, routes and gateways read from the OS; candidate targets derived from connected RFC 1918 interfaces.
›
2
ICMP
sweep
Every address in the candidate prefix probed concurrently with a bounded timeout.
›
3
Neighbor
correlation
ARP cache read after the sweep and merged in, recovering hosts that suppressed ICMP but answered Layer 2.
›
4
Service
probing
A fixed set of common TCP ports tested against each responder with a short connect timeout.
›
5
Classification
and reporting
Hardware prefix, resolved name and service profile combined into a provisional classification. HTML, PDF, CSV, JSON, log.
Classification is evidential, not authoritative. No authenticated fingerprinting is performed — the tool reports the observations an identity may be inferred from, and Slide 9 shows what happens when that inference is wrong.
Notes: Stage 3 is the one that earns its keep: ARP recovers hosts a pure ping sweep would miss entirely.

## Slide 6
Cross-platform tooling
Purpose-built rather than off-the-shelf, so the output format is identical on both platforms.
Windows
PowerShell 5.1
No external module dependencies
Five defects fixed during development, four of them PowerShell 5.1 type semantics rather than logic: null gateway dereference, signed-mask conversion, async task type mismatch, nested result object, empty-array parameter fault
macOS
Bash 3.2
Constrained to POSIX constructs — no associative arrays
Revised from sequential to concurrent probing
Known reporting defect: multicast and broadcast destinations were counted as hosts, inflating device totals
8 min → 27 s
macOS /24 sweep, after moving to concurrent probing
Shared output contract
HTML report · PDF · CSV device inventory · JSON · run log
Notes: Both implementations emit the same artifact set, which is what makes the three inventories directly comparable in the next section.

## Slide 7
Same address. Two devices.
Layer 3 evidence was degenerate. Layer 2 evidence was not.
VANTAGE ON DOMAIN A
gateway 192.168.0.1
hwaddr 3C:6A:D2:XX:XX:XX
VANTAGE ON DOMAIN B
gateway 192.168.0.1
hwaddr 24:2F:D0:XX:XX:XX
Two globally administered hardware addresses cannot belong to one interface.
The two vantage points were resolving the same Layer 3 address to two different physical devices — possible only across separate Layer 2 domains. Domain separation was established without changing anything in the environment, using evidence a Layer 3-only methodology discards.
Notes: This is the single most important slide. If a discovery tool throws away MAC data, it cannot detect this entire class of defect.

## Slide 8
What each vantage point saw
Identical declared prefix, identical gateway address, materially different device populations.
Domain A
seen from the Windows workstation and one Mac mini
192.168.0.1 Gateway A
192.168.0.2 NAS interface LAN 1
192.168.0.45 unidentified, randomized MAC
192.168.0.118 unidentified, persistent
192.168.0.135 Windows workstation
192.168.0.156 unidentified, randomized MAC
192.168.0.201 Mac mini, TCP 5000 open
Domain B
seen from the second Mac mini
192.168.0.1 Gateway B, different hwaddr
192.168.0.8 Mac mini
192.168.0.52 unidentified
192.168.0.56 unidentified, ARP-only
192.168.0.107 unidentified
192.168.0.228 unidentified, TCP 80 open
192.168.0.242 NAS interface LAN 2
Two addresses — .0.2 and .0.242 — presented identical service profiles with hardware addresses differing only in the terminal octet: two NICs on one chassis, assigned consecutively at manufacture. The NAS was in both overlapping domains simultaneously.
Notes: Neither list is wrong. Each is a complete view of one broadcast domain. The comparison, not either inventory, is the diagnostic result.

## Slide 9
A hypothesis that was wrong
Reported here because the correction is itself a result of the method.
OBSERVED
192.168.0.201 responded on TCP 5000 — the storage vendor's unencrypted management port.
›
INFERRED
Probably a second storage appliance. A single weak signal, promoted to an identity.
›
FALSIFIED
The inventory run from that host established it as a Mac mini running an unrelated service on the same port.
Why it stays in the report
It is a concrete demonstration of why a service profile must not be promoted to a device identity.
The correction was produced by the multi-vantage-point method, not in spite of it.
An assessment that reports only its confirmed conclusions overstates its own reliability.
Notes: Interviewers respond well to this slide. It shows a hypothesis being tested and dropped rather than a tidy narrative assembled after the fact.

## Slide 10
Remediation design
Three constraints, and the candidate designs each one eliminated.
Constraints
1
Both upstream services remain independent and in use — consolidation was out of scope.
2
The NAS remains reachable from both domains at line rate, which excludes routing NAS traffic through a gateway.
3
No transit path is created between the domains — each carries its own untrusted upstream.
Designs rejected
Bridge the domains through the NAS
Creates exactly the transit path constraint 3 prohibits, and puts a storage appliance in a forwarding role it was not built for.
Aggregate the two NAS interfaces
Invalid — the interfaces terminate on different switches in different domains, and aggregation requires a single logical peer.
Disable DHCP on one gateway
The standard fix where a second router is an access point. Inapplicable here: each gateway serves its own upstream and must issue leases.
Notes: Being able to say why the obvious fixes are wrong is worth more than the fix itself.

## Slide 11
Before and after
Disjoint prefixes. The physical topology is unchanged.
BEFORE
Gateway A 192.168.0.1/24
NAS LAN 1 192.168.0.2
Gateway B 192.168.0.1/24
NAS LAN 2 192.168.0.242
AFTER
Gateway A 192.168.0.1/24
NAS LAN 1 192.168.0.2
Gateway B 192.168.20.1/24
NAS LAN 2 192.168.20.2 (static)
Single default route retained
The NAS interface on Domain B was deliberately left without a gateway, leaving Domain A as the appliance's only default route.
Upstream untouched
PPPoE credentials and NAT behaviour on Gateway B were not modified.
One transient outage
A stale DHCP lease left the Domain B client asserting a retired prefix across a working link. Shorten lease time before a planned readdressing.
Notes: Gateway A was left alone. 192.168.0.0/24 is still the most common home prefix in existence, so moving it too is a reasonable follow-up if VPN collisions become an issue.

## Slide 12
Validation
Reachability, service availability — and the deliberate absence of transit.
Positive tests
Each gateway and each NAS interface answers echo requests from within its own domain
NAS management confirmed over HTTPS 5001 from both domains
SMB mounts re-established from both domains
Upstream reachability confirmed independently on each service
DHCP confirmed issuing from the correct scope on each gateway
The negative test
Hosts on Domain A remain unable to reach hosts on Domain B, and the converse.
This is the intended outcome. The remediation resolves address ambiguity; it does not — and should not — establish inter-domain connectivity. Conflating the two objectives is the common error in this scenario, so verifying that transit is absent is as much a part of validation as verifying that services are reachable.
Notes: If someone asks why the two networks still cannot see each other, the answer is that this was a design requirement, not a leftover fault.

## Slide 13
Security review
Ratings are qualitative and reflect a residential threat model.
HIGH
Unidentified hosts on both domains
Correlate against gateway client tables; deny anything unaccounted for
MED
Unencrypted management port reachable on the NAS
Restrict to HTTPS 5001; disable the plaintext listener
MED
No host-level firewall policy on the NAS
Permit only 192.168.0.0/24 and 192.168.20.0/24
MED
Single-factor administrative access; default admin account live
Enable a second factor; disable the built-in account
MED
No segmentation for IoT and guest endpoints
Isolate on a guest SSID and deny it access to storage
LOW
Legacy SMB dialect not explicitly disabled
Enforce an SMB2/SMB3 minimum
Unidentified hosts rate highest not because any one of them is known to be hostile, but because an environment whose administrator cannot enumerate what is attached cannot support any access-control assertion at all.
Notes: Two of the unidentified hosts used locally administered MACs, consistent with mobile address randomization — those have to be resolved through the gateway client table, not through scanning.

## Slide 14
What this assessment cannot see
Stated as a result, not as a footnote.
ICMP suppression
Hosts that discard echo requests are invisible to the sweep and are recovered only if they appear in the ARP cache. A fourth workstation in this environment produced a full host diagnostic yet appeared in no inventory — powered down, firewalled, or on an unscanned domain. Unresolved.
Point-in-time sampling
Each inventory is one observation. Devices asleep, disconnected, or in a wireless power-saving state during the sweep are absent by construction. No longitudinal collection was performed.
Address randomization
Locally administered hardware addresses defeat vendor attribution and are not stable across associations, so a randomizing device cannot be tracked between inventories by MAC.
Reporting artifacts
The macOS implementation counted multicast and broadcast destinations among its responders, inflating every published device total from that build. A filter defect, not a discovery defect — but it affects the numbers.
Device classification is evidential throughout: inferred from hardware prefix, resolved name and service profile, none of which is authoritative.
Notes: An inventory presented without its false-negative profile invites overinterpretation. This slide is the reason the rest of the deck can be trusted.

## Slide 15
What comes next
In order of value.
1
Post-remediation collection
Rerun both implementations and diff against the pre-change baseline. Domain B client addresses were reassigned by DHCP and are not derivable from their old values.
2
Resolve every unidentified host
Correlate the remaining unknowns against each gateway's own client table.
3
Static reservations for infrastructure
So the address plan is documented in the DHCP configuration itself rather than in a diagram.
4
Managed switch and VLAN segmentation
The one capability the current unmanaged Layer 2 distribution cannot provide.
5
Centralized logging and availability monitoring
Converts a point-in-time inventory into a continuous one.
Notes: Item 1 blocks items 2 and 3 — everything downstream needs the post-change data first.

## Slide 16
Identical private addresses observed from
different vantage points carry no implication
of identical devices.
And the reverse inference — treating a shared prefix as evidence of a shared domain — is unsound anywhere more than one gateway may exist. Where Layer 3 evidence is degenerate, Layer 2 evidence remains discriminating; a discovery tool that discards hardware-address data forfeits its ability to detect this entire class of defect.
Dual-ISP Network Assessment and Subnet Remediation · Vijaysingh Puwar · Full write-up available as an IEEE-format technical report
Notes: Close on the general lesson rather than on the specific fix — the fix is trivial, the reasoning is what transfers.